## Slide 1: Zigbee

## Slide 2: What is ZigBee?
Technological Standard Created for Control and Sensor Networks
Based on the IEEE 802.15.4 Standard
Created by the ZigBee Alliance

## Slide 3: IEEE 802.15.4
Zigbee is set of high level communication protocols based upon the specification produced by 802.15.4 - standard for wireless personal area networks (WPANs)

## Slide 4: IEEE 802.15.4 & ZigBee In Context
  “the software”
  Network, Security & Application layers
  Brand management
IEEE 802.15.4
  “the hardware”
  Physical & Media Access Control layers
PHY
868MHz / 915MHz / 2.4GHz
MAC
Network
Star / Mesh / Cluster-Tree
Security
32- / 64- / 128-bit encryption
Application
API
ZigBee
Alliance
IEEE
802.15.4
Customer
Silicon
Stack
App

## Slide 5: WPANs
A personal area network (PAN) is a computer network used for communication among computer devices (including telephones and personal digital assistants) close to one person
A wireless PAN consists of a dynamic group of less than 255 devices that communicate within a range of about a 33-feet.

## Slide 6: IEEE 802 Wireless Space

## Slide 7: ZigBee Aims Low
Low data rate
Low power consumption
Small packet devices

## Slide 8: ZigBee Vs Other Wireless Protocols

## Slide 9: ZigBee Vs Bluetooth
Bluetooth targets medium data rate continuous duty
– 1 Mbps over the air, ~700 kbps best case data transfer
– File transfer, streaming telecom audio
– Point to multipoint networking
ZigBee targets low data rate, low duty cycle
– 250 kbps over the air, 60-115 kbps typical data transfer
– Long battery life (weeks to months)
– More sophisticated networking

## Slide 10: ZigBee Applications

## Slide 11: ZigBee Network Model

## Slide 12: Network Pieces : PAN Coordinator
PAN Coordinator(ZC)
• One and only one in PAN
• “owns” the network
•Starts it
• Allows other devices to join it
• Provides binding and address-table services
• Saves messages until they can be delivered
• And more… could also have i/o capability
• A “full-function device” – FFD
• Mains powered

## Slide 13: Network Pieces : Router
Routers(ZR)
• Optional element
Routes messages- Participates in multihop routing of messages.
• Does not own or start network
• Scans to find a network to join
• A “full-function device” – FFD

## Slide 14: Network Pieces : End Devices
End Device(ZED)
• Optional element
Communicates with a single device, does not participate in routing
• Does not own or start network
• Scans to find a network to join
• Can be an FFD or RFD
• Usually battery powered

## Slide 15: IEEE 802.15.4 Device Types
Network Coordinator
Maintains overall network knowledge; most sophisticated of the three types; most memory and computing power
Full Function Device (FFD)
- Carries full 802.15.4 functionality and all features specified by the standard
- Additional memory, computing power make it ideal for a network router function
- Could also be used in network edge devices where the network touches other networks or devices that are not IEEE 802.15.4 compliant
Reduced Function Device (RFD)
- Carriers limited (as specified by the standard) functionality to control cost and complexity
- General usage will be in network edge devices

## Slide 16: Network Topologies

## Slide 17: ZigBee Mesh Networking
Slide Courtesy of
Source: http://www.zigbee.org/en/resources/#SlidePresentations

## Slide 18: ZigBee Mesh Networking
Slide Courtesy of
Source: http://www.zigbee.org/en/resources/#SlidePresentations

## Slide 19: ZigBee Mesh Networking
Slide Courtesy of
Source: http://www.zigbee.org/en/resources/#SlidePresentations

## Slide 20: ZigBee Mesh Networking
Slide Courtesy of
Source: http://www.zigbee.org/en/resources/#SlidePresentations

## Slide 21: AT Mode(What)
AT mode is synonymous with "Transparent" mode.
In AT mode, any data sent to the XBee module is immediately sent to the remote module identified by the Destination Address in memory.
If the XBee that the data is sent to is the Coordinator it will broadcast on the PanID.
No packet formation is necessary, but rather simple send Serial data to the tx of one Xbee and it will be received by the rx of the destination XBee

## Slide 22: AT Mode(Why?)
If you are new to XBees this is the fastest way to start transmitting
If you only communication between two XBees
If you can implement an external protocol

## Slide 23: API Mode(What)
API mode is "Application Programming Interface"
Data must be formatted in frames with Destination information and payload
The API is an alternative to the default transparent mode.

## Slide 24: API Mode(why?)
For larger networks that involve nodes talking to multiple targets
If XBees are gathering data without a mbed attached and thus can not format their own data before sending
If power is a big concern and you would like End Devices to 'sleep' until data is requested.
Need to change parameters without entering command mode (XBee only)
Want to view RSSI and source address on a packet by packet basis
Would like to receive packet delivery confirmation on every transmitted packet

## Slide 25: Simple Chat using AT mode

## Slide 26: Basic Assembly: Plug In an XBee!

## Slide 27: Connect to computer..

## Slide 28: Zigbee point to point communication
1st xbee as router
  Set PAN ID(Say 1234)
  Note SH, SL
  Use SH, SL of coordinator as DH, DL of router
2nd xbee as coordinator
  Set same PAN ID(Say 1234)
  Note SH, SL
  Use SH, SL of coordinator as DH, DL of router

## Slide 29: Launch X-CTU

## Slide 30: X-CTU Test

## Slide 34: Router Configuration

## Slide 36: Router Terminal

## Slide 37: Coordinator set DH DL

## Slide 38: Communication

## Slide 39: Communicate with Arduino

## Slide 40: Router AT- Coordinator API
Components:
  Arduino
  2 XBEE modules
  1 magnetic door lock
  Breadboard
  Resistor

## Slide 41: Coordinator-API configuration

## Slide 42: Router-AT Configuration(1):
v

## Slide 43: Router-AT configuration(2)
v

## Slide 44: Router-AT Configuration(3):
v

## Slide 45: Router AT- Coordinator API

## Slide 46: Co-ordinator Arduino Program:
void loop() {
if(mySerial.available()>21){
for(int i=0;i<22;i++){
Serial.print(mySerial.read(), HEX);
Serial.print(",");
}
Serial.println();
}
// put your main code here, to run repeatedly:
}

## Slide 47: Output:

## Slide 48: Output: Initially

## Slide 49: Output: when disconnected

## Slide 50: References
http://tutorial.cytron.com.my/2012/03/08/xbee-series-2-point-to-point-communication/
https://learn.sparkfun.com/tutorials/exploring-xbees-and-xctu
http://www.learnerswings.com/2014/03/communication-between-xbee-connected-to.html