## Slide 1: What is RFID?
Radio Frequency Identification (RFID) is the Wireless non-contact use of radio-frequency electromagnetic fields to transfer data for the purpose of automatically identifying and tracking tags attached to assets
ADC [Automated Data Collection]

## Slide 2: RFID
RFID, or Radio Frequency Identification, is a system for transferring data over short distances (typically less than 6 inches).
Often only one of the two devices needs to be powered, while the other is a passive device.
This allows for easy use in such things as credit cards, key fobs, and pet collars as there is no need to worry about battery life.
The downside is that the reader and the information holder (i.e credit card) must be very close, and can only hold small amounts of data

## Slide 3: RFID

## Slide 4: Identification
Assign IDs to objects
Link the ID to additional information about the object

## Slide 5: Identification Examples
Bar Codes
License Plates
Social Security Numbers
Student ID
Serial Numbers
Database Key

## Slide 6: RFID System
  Tag Reader - Transceiver
  RFID tag - Transponder
  Antenna [Media interface Layer]

## Slide 7: RFID Hardware
Magnetic / Inductive Coupling
Transceiver
Tag Reader
antenna
RFID
Tag
IC or microprocessor
antenna
Notes: When the tag is placed close enough to the reader the field from the reader coil will couple to the coil from the tag. A voltage will be induced in the tag that will be rectified and used to power the tag circuitry.

## Slide 8: RFID Hardware
Propagation Coupling
Transceiver
Tag Reader
antenna
RFID
Tag
IC or microprocessor
antenna

## Slide 9: Tags
A Tag is a transponder which receives a radio signal and in response to it sends out a radio signal.
Tag contains an antenna, and a small chip that stores a small amount of data
Tag can be programmed at manufacture or on installation
Tag is powered by the high power electromagnetic field generated by the antennas
The field allows the chip/antenna to reflect back an extremely weak signal containing the data
Notes: Two components-

## Slide 10: Types of Tags
Passive Tags
  No battery
  Low cost
Active Tags
  On-board transceiver
  Battery – must be replaced
  Longer range
  High cost

## Slide 11: Different types of tags

## Slide 12: Real Tags

## Slide 13: TAG ATTRIBUTES

## Slide 14: RADIO FREQUENCY IDENTIFICATION (RFID)

## Slide 15: RFID READER/WRITER (RC522)

## Slide 16: MIFARE CARD
Understanding the memory structure of MIFARE Classic cards
The MIFARE Classic card is a memory storage device. The memory is divided into sectors, which are also divided into blocks of 16 bytes.
The MIFARE Classic 1K card has 16 sectors, each of which are divided into four blocks. If we do the math, we can figure out how the memory structure would be like: 16 bytes (1 block) * 4 blocks * 16 sectors = 1024 bytes.
The card reader and the tags communicate using a 13.56MHz

## Slide 17: MIFARE 1K CARD MEMORY STRUCTURE

## Slide 19
#include <SPI.h>
#include <MFRC522.h>
#define SS_PIN 10
#define RST_PIN 9
MFRC522 mfrc522(SS_PIN, RST_PIN); // Create MFRC522 instance.
void setup() {
Serial.begin(9600); // Initialize serial communications with the PC
SPI.begin(); // Init SPI bus
mfrc522.PCD_Init(); // Init MFRC522 card
Serial.println("Scan PICC to see UID and type...");
}

## Slide 20
void loop() {
// Look for new cards
if ( ! mfrc522.PICC_IsNewCardPresent()) {
return;
}
// Select one of the cards
if ( ! mfrc522.PICC_ReadCardSerial()) {
return;
}
// Dump debug info about the card. PICC_HaltA() is automatically //called.
mfrc522.PICC_DumpToSerial(&(mfrc522.uid));
}

## Slide 22: Current Applications
Livestock Tagging
Wild Animal Tracking
Electronic Article Surveillance (EAS)
Automated Toll Collection
Vehicle Anti-Theft

## Slide 23: More Applications
Passive / Secure Entry
Airline Baggage Tracking
Postal Package Tracking
Time and Attendance

## Slide 24: Livestock Tagging
Meet Bobby the Cow
Bobby has an old fashioned ear tag for identification.

## Slide 25: Bobby’s Part of a Herd

## Slide 26: Automated Toll Collection

## Slide 27: Package Tracking
Picture courtesy Texas Instruments

## Slide 28: Potential Applications
Smart Grocery Store
Smart Kitchen

## Slide 29: Smart Grocery Store
Every item in the store already has a bar code.
Why not use an RFID tag?
Speed up checkouts

## Slide 30: Smart Grocery Store
Several carts this full in early evening could seriously slow down the checkout process.
How much do cashiers cost?

## Slide 31: Smart Grocery Store
Add an RFID tag to all items in the grocery.
As the cart leaves the store, it passes through an RFID transceiver
The cart is rung up in seconds.

## Slide 32: Smart Groceries Enhanced
Track products through their entire lifetime.
Diagram courtesy How Stuff Works

## Slide 33: RFID’s Advantages
Passive
  wireless
Store data on a tag
Can be hidden
Work in harsh environments
Low cost?

## Slide 34: RFID’s Disadvantages
Lack of standards!
Short range
Cost